## Slide 1
Force feedback software
Software Architecture Overview
The Force Feedback Fast Loop
The Force Feedback Equations

## Slide 2
Software Architecture Overview
1/2
Flight Gear
Model
Flight Gear
Communication
Channel
Console Acquisition
Application
Slow Loop
Thread
Fast Loop
Thread
Shared Memory

## Slide 3
Software Architecture Overview
2/2
The slow loop (100 Hz) deals with:
  Receiving data from Flight Gear Channel.
  Acquiring data from the Flight Console.
  Putting data in shared memory for the fast loop.
  Getting data in shared memory from the fast loop.
  Sending data through Flight Gear Channel.
The fast loop (2000 Hz) deals with:
  Acquiring data from the force feedback sensors.
  Getting data in shared memory from the slow loop.
  Computing the force feedback values.
  Computing the force feedback actuators voltages.
  Putting data in shared memory for the slow loop.

## Slide 4
Force Feedback Fast Loop
1/8
The fast loop location:
  “hfCommandHandle” function in “main.cpp” file from “ConsoleAcquition” project.
The fast loop steps:
  Get data from cockpit IO.
  Get inputs from FG model.
  Compute actuators inputs.
  Write outputs.
Get data from cockpit IO
Get inputs from FG model
Compute actuators inputs
Write outputs

## Slide 5
Force Feedback Fast Loop
2/8
Get data from cockpit IO:
  Use the NI DAQ card driver interface to read:
    Load cell voltage.
    Position sensor voltage.
  Calibrate these values to make them “usable”:
    Load in Newton using “LoadCellVoltageToPilotForce” token (from “FFBConfigTab.xml”).
    Position in [-1,+1] range using “positionSensorRange” token (from “FFBConfigTab.xml”).
  Filters theses values using a Kalman filter.
Get data from cockpit IO
Get inputs from FG model
Compute actuators inputs
Write outputs

## Slide 6
Force Feedback Fast Loop
3/8
Get inputs from FG model:
  Read in shared memory the “ForceFeedBackData_t” structure :
    Counter : integer used to know if the input has been refreshed.
    FFBInputs : FGNetFFBInputs structure.
    Aileron, elevator and rudder trim values (from flight console).
    useFileInputState : boolean indicating if an input file is to be used.
    fileInputState : FileInputState_t structure containing input file data (see chapter 7 of the User Manual).
Get data from cockpit IO
Get inputs from FG model
Compute actuators inputs
Write outputs

## Slide 7
Force Feedback Fast Loop
4/8
FGNetFFBInputs structure:
    qbar_psf : dynamic pressure
    rdot_rad_sec, qdot_rad_sec, pdot_rad_sec: body angular accelerations
    psidot_rad_sec, thetadot_rad_sec, phidot_rad_sec: angular rates
    a_pilot_x_ft_sec2, a_pilot_y_ft_sec2, a_pilot_z_ft_sec2: pilot accelerations
    elevator_pos_rad, right_aileron_pos_rad, rudder_pos_rad: control surfaces position
    v_north_fps, v_east_fps, v_down_fps: aircraft speed
    p_rad_sec, q_rad_sec, r_rad_sec: body angular rates
    u_fps, v_fps, w_fps: CG’s body velocity components
    gz, gy: z and y acceleration on body axis
    wdot_fps, vdot_fps: CG’s body accelerations components
    alpha_rad, beta_rad: angles of attack
    vt_fps: air speed
    latitude_deg, longitude_deg, altitude_m: geodetic position
    phi_rad, theta_rad, psi_rad
Get data from cockpit IO
Get inputs from FG model
Compute actuators inputs
Write outputs

## Slide 8
Force Feedback Fast Loop
5/8
Compute actuators inputs:
    Compute pilot force:
      If load < frictionThreshold: pilot force = 0
      Else pilot force =load cell - frictionThreshold.
    Compute FFB: “ComputeFFB” function of “CFFBConfig” class in “FFBConfig.cpp” file.
    Compute force to apply on actuator:
      Total force = pilot force + ffb
      Actuator force = assistGain * Total force
      The “assistGain” is a multiplication factor applied to the actuator force to “remove” the force feed back real system inertia and friction.
Get data from cockpit IO
Get inputs from FG model
Compute actuators inputs
Write outputs

## Slide 9
Force Feedback Fast Loop
6/8
Compute actuators inputs:
    Filter actuator order to take into account former values: ponderated average like
      Where:
      h is an “hysteresis ratio” (0 = no hysteresis, 0.999 = a lot of hysteresis). Its value is set to 0.5.
      rawOrder is the computed order before filtering.
      ordern is the filtered order in the current loop, ordern-i is the filtered order a the “ith” former loop.
Get data from cockpit IO
Get inputs from FG model
Compute actuators inputs
Write outputs

## Slide 10
Force Feedback Fast Loop
7/8
Compute actuators inputs:
    Softly reduce actuator order before bounds using “softwareBoundLimitationStart”:
      If the command position exceeds the limitation bound and the actuator is in the direction of the bound, then the actuator orders is multiply by:
    Limit actuator order variation using “actuatorMaxVoltageSpeed” token to get a smooth actuator motion:
      If the new order has the same direction as the former one | new actuator order - former actuator order | is limited to (actuatorMaxVoltageSpeed * dt)
      Else | new actuator order - former actuator order | is limited to 10 * (actuatorMaxVoltageSpeed * dt)
Get data from cockpit IO
Get inputs from FG model
Compute actuators inputs
Write outputs

## Slide 11
Force Feedback Fast Loop
7/8
Write outputs:
  Write actuator order using the NI DAQ card driver interface.
  Write FFB outputs:
    FFB computation input data.
    FFB computation output data.
    FFB computation intermediate data.
    Other relevant data.
    Written in the output file of the record functionality
    (see chapter 7 of the User Manual).
Get data from cockpit IO
Get inputs from FG model
Compute actuators inputs
Write outputs

## Slide 12
Force Feedback Equations
See chapter 8 of the User Manual