## Slide 1
Force feedback hardware maintenance
How to change force feedback motors belts
How to tune the force feedback motors gears
How to calibrate the force feedback system

## Slide 2
How to change force feedback motors belts
1/5
What you need :
7/64’’ Allen wrench
Cruciform screwdriver
Hammer
Pin remover
What you may need :

## Slide 3
  Make sure to get the black plastic rings that fall down when you remove the pin!
Step 1: remove the pin at the motor bottom
How to change force feedback motors belts
2/5
  Remove the locking metal rings.
  Remove the pin using the pin remover if needed.

## Slide 4
  Unscrew the 6 screws. Make sure to get the screws!
Step 2: dismount the motor bottom
How to change force feedback motors belts
3/5
  Remove the motor bottom

## Slide 5
Step 3: replace the old belt
How to change force feedback motors belts
4/5
  Loosen slightly the 4 screws with the Allen wrench. Make sure not to remove the screws!
  Replace the old belt with the new one.
  Move the motor to unbend the belt.

## Slide 6
  Move the motor to bend the belt. Make sure not to over bend the belt or you will damage the new belt!
  Remount the pin with its black plastic rings and its locking metal rings. Make sure not to forget to replace the rings!
Step 3: remount the motor
How to change force feedback motors belts
5/5
  Remount the motor bottom and the 6 screws.
  Tighten the 4 screws.

## Slide 7
When to do it ?
  When the force feedback has lost strength.
  When the force feedback motor belt seems to slip.
How to be sure ?
  Check it with the force feedback calibration software.
How to tune the force feedback motors gears
1/2

## Slide 8
How to do it ?
1. Turn the gear screw by a maximum
value of 90° to tighten it.
2. Remount the system and test it again.
3. Tighten the gear screw again if needed.
Cleaning
If needed you may remove the gear screw to clean the gear mechanism.
How to tune the force feedback motors gears
2/2
In this case, make sure to replace every part of it
in the right order.
If the gear is too tight you may
damage the belt!

## Slide 9
How to calibrate the force feed back system
1/7
The calibration deals with :
  Voltage to Force and Force to Voltage conversions.
  Motion range.
  Force feedback sensibility.
The calibration data are to be set in the “FFBConfigTab.xml” file.
The “Calibration Tool” software is needed to get the calibration data.

## Slide 10
How to calibrate the force feed back system
2/7
Voltage to Force conversion : load cell voltage to pilot force
    “LoadCellVoltageToPilotForce” token:
      Conversion table from load cell voltage (V) to Pilot Force (N).
      Positive values only.
    “loadCellPositiveVoltageDirection” token:
      Direction corresponding to a positive voltage of the load cell :
        “forward” or “backward” for a translation (elevator and rudder).
        “clockwise”, “counterclockwise” for a rotation (aileron).

## Slide 11
How to calibrate the force feed back system
3/7
Force to Voltage conversion : feedback computed force to actuator voltage
    “FeedbackForceToActuatorVoltage” token:
      Conversion table from computed force (N) to actuator voltage (V).
      Positive values only.
    “actuatorPositiveVoltageDirection” token:
      Direction corresponding to a positive voltage applied to the actuator :
        “forward” or “backward” for a translation (elevator and rudder).
        “clockwise”, “counterclockwise” for a rotation (aileron).

## Slide 12
How to calibrate the force feed back system
4/7
Motion range : “positionSensorRange” token.
  “minValue” sub-token :
  Voltage measured by the position sensor in the most left position for rotation or the most backward position for translation.
  “maxValue” sub-token :
    Voltage measured by the position sensor in the most right position for rotation or the most forward position for translation.

## Slide 13
How to calibrate the force feed back system
5/7
Force feedback sensibility :
  “frictionThreshold” token: value (N) under which the force given by the load cell is regarded as “friction noise”.
  “softwareBoundLimitationStart” token: relative command position value ([0;1]) beyond which the command is stopped. Used to prevent the actuator to “hit” its physical bounds.
  “actuatorMaxVoltageSpeed” token: maximum actuator voltage variation (V/s). Used to a get smooth actuator motion.
  “assistGain” token: multiplication factor applied to the actuator force to remove the force feed back real system inertia and friction

## Slide 14
How to calibrate the force feed back system
6/7
The calibration tool
Select command
Set actuator voltage step and validate
Increase/decrease actuator voltage
(by the value of the step)
Read actuator voltage value
Stop actuator
(set voltage value to 0)
Read sensors voltage values
Use automatic calibration for load cell voltage values (to have a zero voltage for a zero load)
ALWAYS SWITCH POWER ON BEFORE LAUNCHING THE CALIBRATION TOOL

## Slide 15
Please remind the actuator maximum forces :
  Yoke translation : 613 N.
  Yoke rotation: about 800N at pilot hands (80N.m moment)
  Rudder pedal translation : 971 N.
How to calibrate the force feed back system
7/7
Calibration procedure :
Install a dynamometer to measure the force.
Use the calibration tool to :
  Increase step by step the actuator voltage value.
  Read the actuator voltage.
  Read the corresponding force on the dynamometer.
  Read the corresponding load cell on the calibration tool.
  Make sure to check “Automatic Calibration” to have a zero voltage for a zero load.
Set the values in the “FFBConfigTab.xml” file.
Repeat the operation for each axis.